Remote Keyboard User Manual:

First use:
Board is shipped with settings preconfigured, that is,it waits for DHCP settings. Therefore it should be connected to an access point through standard Ethernet cable and reconfigured through desktop application. To restore factory settings user should push and hold blue button until resetting message appears.
Power :
Board requires separate usb power supply through usb marked as ‘USB ST-Link’.
To save power, screen is automatically turned off after 30 seconds of inactivity. In order to turn it back on click blue button.
Connectivity:
Facilities of mouse and keyboard are supplied throught ‘USB_FS’ connector. It should be connected to client computer.
Known issues:
Hot plugging Ethernet cable requires restart of the device.
Sometimes during first initialization in DHCP mode board shows server address as ‘0.0.0.0’. In order to fix this issue board should be restarted.